## Slide 1
GUJARAT STATE HACKATHON 2026
EyesOnGuj
One Platform. Every Camera. Zero Blind Spots.
AI-Powered, Vendor-Agnostic Video Intelligence for Gujarat's Statewide CCTV Grid
Built for Sentinels: Integrated Video Management & Analytics Platform for Government CCTV Integration | Gujarat State Hackathon 2026

## Slide 2
THE PROBLEM
Gujarat Has 80,000+ Cameras. It Has Zero Unified Intelligence.
Every department solved surveillance alone. Nobody solved it together.
80,000+ cameras, 0 shared registry.
Departmental RTSP feeds, ONVIF hardware, and vendor VMS platforms (Milestone, HikCentral, Dahua-class) each operate in isolation, with no single source of truth for what exists, where it is, or whether it's even online.
3+ incompatible vendor payload formats.
Milestone calls it licensePlate. HikCentral calls it plateText. Dahua calls it plate. Every integration today is a custom, one-off engineering project. There is no standard adapter layer.
0 cross-camera intelligence.
A stolen vehicle spotted on a Home Department camera and again on an RTO camera 40km away gets treated as two unrelated events. No system today stitches a route across departments or vendors.
Manual, reactive watchlist checks.
Vehicle and person watchlist matching happens after the fact, if at all. Not in real time, not automatically, not at platform scale.
"The cost of fragmentation isn't inefficiency. It's a missed window on a live threat."

## Slide 3
THE SOLUTION
EyesOnGuj: One FastAPI Platform. Three Integrated Engines. One Shared Brain.
Not three disconnected tools bolted together. Three models sharing one schema, one login session, one RBAC layer, and one deployment unit.
MODEL 1: REGISTRY & GIS
1 unified camera registry
Department- and district-scoped camera CRUD, bulk CSV onboarding, and real PostGIS-powered coverage gap analysis using 1km geodesic buffer computation. Not a static map. An actual spatial query engine.
MODEL 2: LIVE AI ANALYTICS
512-dimensional face embeddings, real-time
Direct RTSP ingestion, YOLO + ByteTrack vehicle detection, ANPR with Indian/Bharat-series plate validation, and a 5-gate face quality pipeline feeding pgvector HNSW similarity search. WebSocket alerts hit operators the instant a watchlist match fires.
MODEL 3: MULTI-VMS FEDERATION
Zero new code for supported protocols
An adapter pattern (ONVIF, REST/API-key, municipal, police, RTO) that onboards any already-supported vendor system through configuration alone, plus a correlation engine that deduplicates and reconstructs cross-camera, cross-VMS vehicle routes via plate + timestamp joins.
"A direct RTSP camera and a federated vendor camera write into the exact same

## Slide 4
HOW IT WORKS
From Camera to Command Center in Under a Second
The full pipeline, end to end. No manual steps, no batch delay.
01
ONBOARD
A camera enters the platform one of two ways: direct RTSP ingestion (Model 2 spins up one dedicated stream worker per camera) or federated onboarding through a vendor adapter (Model 3), with a live test-connection check before anything is persisted.
02
REGISTER
The camera lands in the shared registry with department, district, GPS location, ownership, and retention metadata. It's instantly visible on the GIS map and included in the next coverage gap analysis pass.
03
DETECT
Live video gets analyzed frame by frame. YOLO + ByteTrack for vehicle detection and multi-object tracking, OCR-based ANPR for plate reads, and a 5-gate quality pipeline (face detection plus solvePnP 3D pose validation) for facial capture.
04
MATCH
Every detection is checked in real time against the vehicles_watchlist and persons_watchlist tables. Plate-string matching for vehicles, 512-d cosine-similarity search over a pgvector HNSW index for faces.
05
CORRELATE
Matches and raw sightings alike flow into the correlation engine, which deduplicates events, resolves identity across cameras, and stitches cross-camera, cross-VMS routes using plate + timestamp joins, regardless of which department's camera or which vendor's VMS captured the sighting.
06
ALERT
A confirmed match triggers a severity-scored alert, broadcast via WebSocket to every connected operator dashboard in real time. GIS map, live camera grid, and federation console update simultaneously. Zero polling. Zero delay.
6 steps. 3 models. 1 unified pipeline, from first frame to operator alert.

## Slide 5
DATA ARCHITECTURE
One Schema. Twelve Tables. Zero Data Silos.
Every model reads and writes the same PostgreSQL 16 database. There is no "Model 1 database" and "Model 2 database."
CORE REGISTRY LAYER
departments: government department directory (Home/Police, RTO, Municipal Corporation, and more)
districts: all of Gujarat's 33 districts, each with a PostGIS MULTIPOLYGON boundary for spatial queries
users: role-based accounts (dept_admin, operator, viewer)
cameras: the central hub table. Registry fields, grid-sync fields, and VMS-linkage fields, all on one row per camera
vms_systems: one row per federated vendor VMS integration, tracking vendor, protocol, adapter type, and live connection status
status_history: full trigger-written audit trail of every camera change
LIVE ANALYTICS LAYER
vehicles_watchlist: stolen / wanted / blacklisted plate registry
persons_watchlist: wanted / missing / suspect registry with a 512-dimension VECTOR face embedding column
vehicle_tracks: resolved global vehicle identity across sightings, with its own appearance embedding for fallback re-identification
detections: every individual sighting. Plate read, confidence score, cropped image, raw vendor payload preserved for audit
alerts: vehicle-watchlist match events with severity scoring and operator acknowledgment tracking
person_alerts: face-watchlist match events with similarity score and cosine distance recorded per match
12 tables, 1 schema
512-D vectors, HNSW-indexed for sub-linear similarity search
PostGIS geography types on 3 tables. Real spatial math, not lat/lng strings

## Slide 6
KEY FEATURES
Built to Actually Ship, Not Just Demo
Unified Camera Registry
One CRUD interface, full department/district-scoped RBAC, bulk CSV import with row-level validation and partial-success reporting.
Real Geospatial Gap Analysis
PostGIS geodesic 1km-buffer computation identifies actual coverage gaps. Not a heatmap guess.
Live Dual-Modality AI Detection
Simultaneous vehicle detection (YOLO + ByteTrack) and face detection (5-gate quality pipeline + 512-d embeddings) on live and pre-recorded feeds up to 2GB per upload.
Cross-Camera Route Reconstruction
Plate + timestamp joins reconstruct a vehicle's path across cameras and across vendor VMS boundaries. Something no single-vendor VMS can do today.
Zero-Code Vendor Onboarding
Any ONVIF-compliant device or generic REST camera API onboards through a configuration form and live test-connection check. No new adapter code required.
Sub-Second Real-Time Alerting
WebSocket-pushed alerts hit every connected operator dashboard the instant a watchlist match is confirmed. No polling, no refresh delay.

## Slide 7
COMPETITIVE ADVANTAGE
Why Not Just Use [Vendor]'s Own VMS?
Capability | Legacy Single-Vendor VMS | EyesOnGuj
Data model | Siloed per vendor, per department | 1 shared schema across every department and vendor
Vendor lock-in | Locked to one vendor's ecosystem and roadmap | Vendor-agnostic adapter pattern. Swap or add vendors without touching core code
Cross-system correlation | Not possible. No shared identity model | Native cross-camera, cross-VMS route reconstruction via plate + timestamp joins
Coverage analysis | Manual, spreadsheet-driven, or absent | Automated PostGIS 1km-buffer geodesic gap analysis
Time to onboard a new vendor system | Weeks of custom integration engineering | Zero new code for already-supported protocols (ONVIF/REST). Configuration only
Biometric watchlist matching | Rare, batch-based, or manual | Real-time 512-d cosine-similarity face matching over a pgvector HNSW index
"This isn't a better camera dashboard. It's the interoperability layer Gujarat's CCTV estate has never had."

## Slide 8
TECH STACK
Production-Grade Stack, Zero Shortcuts
BACKEND
FastAPI, Python 3.12, SQLAlchemy 2.0 + GeoAlchemy2
DATA LAYER
PostgreSQL 16, PostGIS 3.4, pgvector (HNSW indexing), Redis (event bus & cache)
AI / COMPUTER VISION
YOLO object detection, ByteTrack multi-object tracking, OCR-based ANPR with Indian/Bharat-series plate validation, 5-gate face quality pipeline, 512-d face embedding model
FRONTEND
Server-rendered Jinja2 templates, HTMX, Alpine.js. Zero Node.js build step, zero client-side framework bloat
INFRASTRUCTURE
Docker Compose (single-command deployment), Caddy (automatic TLS termination), WebSocket real-time channels
No Node.js. No React. No client build pipeline. One

## Slide 9
ROADMAP
From Pilot to Statewide, With Security Built In, Not Bolted On
1
PHASE 1 — NOW (PILOT)
Single-host deployment: Caddy to FastAPI application to PostgreSQL/Redis/MediaMTX. All 3 models live and integrated. Demo-ready across the full pipeline: registry, live detection, watchlist matching, and federation.
2
PHASE 2 — NEXT (HARDENING)
At-rest encryption for watchlist and detection tables. Application-layer encryption for stored VMS credentials, replacing today's plaintext config storage. Network segmentation between the VMS-ingestion network and the public dashboard network. Edge-level API gateway and rate limiting.
3
PHASE 3 — STATEWIDE SCALE
Horizontally scaled deployment: load balancer, multiple app instances, a central Postgres cluster, and regional edge nodes for media relay positioned near camera clusters across all 33 districts. Appearance-based re-identification fallback for cases where OCR fails mid-route. Analog camera ingestion. Live disaster recovery with regional replication and tested failover.

## Slide 10
THE ASK / VISION
80,000 Cameras. One Intelligence Layer.
EyesOnGuj doesn't ask Gujarat's departments to replace what they've already built. It asks them to connect it, turning every existing RTSP feed, every ONVIF device, every vendor VMS already deployed statewide into one coordinated, correlated, real-time intelligence layer.
"We're asking for one pilot department and 30 days to prove it live on real infrastructure. Not a slide deck."
Built for Sentinels, because the next threat won't wait for departments to compare notes.